## Slide 1: ENGINEERING MECHANICS
UNIT-II Chapter – 5
STATIC FRICTION
Basanagouda I Patil
Assistant Professor
School of Civil Engineering

## Slide 2
What is Friction?
When a body slide or tend to slide on a surface it is resting , a resisting force opposing the motion is produced at the contact surface. This resisting force is called friction or frictional force.
Block
Rough floor
Applied force P
Motion
Frictional force F

## Slide 3
In the absence of friction, it would be impossible for us to walk, ride a vehicle or pick some object from floor.
In some cases frictional force causes energy loss, which leads to wear & tear of components which are in contact. In such cases frictional force must be reduced.
To reduce friction, lubricants are used in machines.
Fine powder on the carrom board reduces friction.
Thus,
“Friction can be our friend or it can be an evil depending upon the circumstance”

## Slide 4
Types of friction
In general, friction can be classified as :
Dry Friction: It is the force that opposes motion of one solid surface sliding across another solid surface which are in contact.
Fluid friction: It is the force that resists motion either within the fluid itself or of another medium moving through the fluid.

## Slide 5
Further Dry Friction is classified into following two types
Static friction
Dynamic friction
Sliding friction
Rolling friction

## Slide 6
1. Static friction
Friction experienced by the body when it is at rest is called static friction.
Here applied force is less than the limiting friction, hence the body remains at rest.
Ex: Pushing the wall.
Limiting friction
The maximum friction force that can be developed at the contact surface, when body is just on the point of moving is called as limiting friction.
Applied Force P
Static friction F
No
Motion

## Slide 7
Small horizontal force P applied to block will produce static frictional force F and block remain stationary, in equilibrium.
As P increases, the static-frictional force F increases as well until it reaches a maximum value Fm which is limiting frictional force.
Further increase in P causes the block to begin to move as F drops to a smaller dynamic frictional force Fk. and it remains constant further.
Applied Force P
Frictional force F
F
P
Fm
Fk
Equilibrium
Motion
O

## Slide 8
2. Dynamic friction (Fk)
Friction experienced by the body when it is in motion is called dynamic friction.
Here applied force exceeds the limiting friction, hence the body starts moving over another body.
i. Sliding friction
Friction experienced by the body when it sides over the other body is called as sliding friction.
Ex: A person sliding down a slide.
.
Sliding friction
Sliding Motion

## Slide 9
ii. Rolling friction
Friction experienced by the body when it rolls over the other body is called as rolling friction.
Ex: When car moves on the floor, wheels experience rolling friction.
Roller skates used for skating.
Applied Force
Rolling friction
Rolling
Motion

## Slide 10
Coefficient of friction (µ):-
It is the ratio of limiting frictional force and the normal reaction between the objects. Mathematically it is expressed as;
Coefficient of friction = F/N
µ = F/N
Box
Rough floor
P
F
N
P = Applied force
F = Frictional force
N = Normal reaction

## Slide 11
Laws of friction:
Coulomb conducted some experiments & the results of these experiments are known as laws of dry friction or Coulomb’s laws of friction.
The frictional force always acts in the direction opposite to that in which the body tends to move.
Till the limiting value is reached, the magnitude of frictional force is exactly equal to the applied force which tends to move the body.

## Slide 12
3. The magnitude of liming friction bears a constant ratio to the normal reaction between the two surfaces of contact and this ratio is called coefficient of friction.
4. The force of friction depends on roughness or smoothness of the surfaces.
5. The force of friction is independent of the area of contact between the two surfaces.
6. After the body starts moving , the dynamic friction comes into play, the magnitude of which is less than that of liming friction and it bears a constant ratio with normal reaction. This ratio is called coefficient of dynamic friction.

## Slide 13
Angle of Friction:
Consider a block subjected to pull ‘P’ as shown in the above figure. Let ‘F’ be the frictional force developed and ‘N’ be the normal reaction. At contact surface, the reactions are ‘F’ & ‘N’. These two reactions can be combined to get the resultant reaction ‘R’ which acts at angle ‘θ’ to the normal reaction.
P
F
N
W
R
θ

## Slide 14
Thus, tanθ = F/N
As the frictional force increases, the angle θ increases & it can reach a maximum value ‘α’ when limiting value of friction is reached.
Thus, tanα = Fm/N = µ
Therefore, tanα = µ -----(a)
This value of ‘α’ is called as angle of friction.
The angle of friction is defined as that angle made by the resultant reaction ‘R’ with the normal component of reaction ‘N’ when friction reaches its maximum value..

## Slide 15
Angle of Repose:
We know that when grains such as food grains, sand, cement, soil etc are heaped, there exists a limit for the inclination of the heap. Beyond which the grains starts rolling down. The limiting angle up to which the grains repose is called as angle of repose.
Consider a block of weight ‘W’ which is resting on an inclined plane which makes an ‘θ’ with the horizontal.
F
N
W
θ
Wcosθ
Wsinθ
θ

## Slide 16
When ‘θ’ is small, block rests on an inclined plane. As ‘θ’ is increased gradually, at one particular stage, the block starts sliding. The angle made by the plane with the horizontal is called angle of repose for the contact surfaces. Thus “the maximum inclination of the plane on which a body free from external forces, can repose is called Angle of Repose”.
Now to prove that angle of repose is equal to limiting angle of friction consider equilibrium of block which is show in the above figure.

## Slide 17
Applying equilibrium equations:
∑Fx= 0 i.e Forces parallel to plane = 0
F-Wsinθ = 0
F = Wsinθ -------- (i)
∑Fy= 0 i.e Forces normal to plane = 0
N - Wcosθ = 0
N = Wcosθ ------- (ii)

## Slide 18
Let ϕ be the value of ‘θ’ such that the maximum frictional force Fm is called into play. and the motion is impending hence
tanϕ = Fm/N
tanϕ = Wsinϕ/ Wcosϕ = µ
tanϕ = µ ------(b)
From (a) and (b) we have tanα = tanϕ
=> α = Φ
Thus value of limiting angle of friction is same as the angle of repose

## Slide 19
Cone of friction:
When the body is having impending motion in the direction of applied force ‘P’, the frictional force will be limiting friction & the resultant reaction ‘R’ will make limiting frictional angle α with the normal reaction.
If the body is having impending motion in some other direction, the resultant reaction ‘R’ will make limiting frictional angle α with the normal reaction.
P
F
N
W
R
α
α

## Slide 20
Thus, if the direction of force ‘P’ is gradually changed through 3600, the resultant ‘R’ generates a right circular cone with semi central angle equal to ‘α’.
If the resultant reaction ‘R’ lies on the surface of this inverted cone whose semi central angle is limiting frictional angle ‘α’ the motion of the body is impending. If the resultant is within this cone the body is stationary. This inverted cone with semi central angle equal to limiting frictional angle ‘α’ is called Cone of Friction.

## Slide 21
Problem 1.0
A body of weight W = 500 N is pulled up an inclined plane by a force of P = 350 N. The inclination of the plane is θ = 300 to the horizontal & the force is applied parallel to the plane. Determine the coefficient of friction.
P
θ

## Slide 22
Solution:
Let us first draw the Free body diagram (FBD) and understand different forces and reactions acting on the block.
P = 350 N
θ
FBD
W = 500 N
+X
-X
+Y
-Y
F
N
W = 500 N
500cosθ
500sinθ
θ

## Slide 23
Since the applied force is pulling the bock up the plane it is at impending motion. Resolving forces in X and Y directions.
∑Fx= 0
P – F – 500sinθ = 0
350 – F – 500sin30 = 0
F = 100 N
∑Fy= 0
-500cos30 + N = 0
N = 433.012 N
At limiting equilibrium condition
Coefficient of friction, µ = F/N
µ = 100/433.012
µ = 0.2309
P = 350 N
θ
W = 500 N
F
N

## Slide 24
Problem 2.0
The coefficient of friction between 20 kg block and incline are µS = 0.4 and µK =0.3. Determine whether the block is in equilibrium if P= 400 N & θ =30° as shown and find the magnitude & direction of friction force.

## Slide 25
Solution:
Let us first draw the Free body diagram (FBD) and understand different forces and reactions acting on the block.
P
FBD
196.2 N
N
400
300

## Slide 26
Net force acting along the plane,
196.2sin30 – 400cos40
= -208.31 N (acting up the plane)
Hence the body is having tendency to move up the plane.
For equilibrium frictional force required is Freq = 208.31 N acting
Down the plane.
Net force acting perpendicular to the plane,
-196.2cos30 – 400sin40 + N = 0
N = 427 N
Frictional force at limiting equilibrium condition is
Fm= µsN
Fm= 0.4*427
= 170.80 N
Since Fm< Freq the block will not be in equilibrium and is moving up the plane.
Hence, the frictional force during the motion, Fk = µkN = 0.3 * 427 = 128.10 N down the plane.
P
FBD
196.2 N
N
400
300

## Slide 27
Problem 3.0
A block is acted upon by two forces as shown. Knowing that the coefficients of friction between the block and the incline are µS = 0.35 and µK =0.25, determine the force P required (a) to start the block moving up the incline, (b) to keep it moving up, (c) to prevent it from sliding down.

## Slide 28
Solution: (a) to start the block moving up the incline
Let us first draw the Free body diagram (FBD) and understand different forces and reactions acting on the block.
P
FBD
800 N
+X
-X
+Y
-Y
F
N
250
800sin25
800cos25
250
250
800 N
250
motion
250
Psin25
Pcos25
P

## Slide 29
The body is in static condition hence Fm = µsN
∑Fx= 0
F + 800sin25 – Pcos25 = 0
F = Pcos25 – 800sin25
WKT F = µsN = 0.35N
0.35N = Pcos25 – 800sin25 --------(i)
∑Fy= 0
N – 800cos25 – Psin25 = 0
P
FBD
800 N
F
N
250
250
250
motion
800sin25
800cos25
800 N
250
250
Psin25
Pcos25

## Slide 30
N = 800cos25 + Psin25 -----(ii)
Substituting (ii) in (i)
0.35[800cos25 + Psin25] = Pcos25 – 800sin25
0.758P = 591.86
P = 780.82 N
P
FBD
800 N
F
N
250
250
250
motion

## Slide 31
(b) To keep it moving up:
Since body is moving up, coefficient of dynamic friction should be considered.
Fk = µkN
P
FBD
800 N
+X
-X
+Y
-Y
F
N
250
800sin25
800cos25
250
250
800 N
250
motion
250
Psin25
Pcos25

## Slide 32
∑Fx= 0
F + 800sin25 – Pcos25 = 0
F = Pcos25 – 800sin25
WKT F = µkN = 0.25N
0.25N = Pcos25 – 800sin25 --------(i)
∑Fy= 0
N – 800cos25 – Psin25 = 0
P
FBD
800 N
F
N
250
250
250
motion
800sin25
800cos25
800 N
250
250
Psin25
Pcos25

## Slide 33
N = 800cos25 + Psin25 -----(ii)
Substituting (ii) in (i)
0.25[800cos25 + Psin25] = Pcos25 – 800sin25
0.8P = 519.351
P = 649.188 N
P
FBD
800 N
F
N
250
250
250
motion

## Slide 34
(c) To prevent it from sliding down:
To prevent it from sliding down means the block should be under static condition.
Fm = µsN
P
FBD
800 N
+X
-X
+Y
-Y
F
N
250
800sin25
800cos25
250
250
800 N
250
motion
250
Psin25
Pcos25

## Slide 35
∑Fx= 0
-F + 800sin25 – Pcos25 = 0
F = 800sin25 - Pcos25
WKT F = µsN = 0.35N
0.35N = 800sin25 - Pcos25 --------(i)
∑Fy= 0
N – 800cos25 – Psin25 = 0
800sin25
800cos25
800 N
250
250
Psin25
Pcos25
P
FBD
800 N
F
N
250
250
250
motion

## Slide 36
N = 800cos25 + Psin25 -----(ii)
Substituting (ii) in (i)
0.25[800cos25 + Psin25] = 800sin25 - Pcos25
1.054P = 84.328
P = 80 N
P
FBD
800 N
F
N
250
250
250
motion

## Slide 37
Problem 4.0
The coefficients of friction between the block and the rail are µS = 0.3 & µK =0.25. Find the magnitude and direction of the smallest force P required to (i) start the block up the rail and (ii) to keep it from moving down.

## Slide 38
Solution: Case(i) to start the block moving up the incline
Considering the limiting equilibrium, the FBD of block is as shown. Since the motion impends up the plane the frictional force acts down the plane.
P
FBD
500 N
FA
N
500sin35
500cos35
350
350
motion
350
500
+X
-X
+Y
-Y
(θ – 350)

## Slide 39
Resolving the forces perpendicular to the plane,
∑Fy= 0
N – 500cos35 + Psin(θ – 350) = 0
N = 409.57 - Psin(θ – 350)
But F = µsN = 0.3[409.57 - Psin(θ – 350)]
F = 122.87 – 0.3Psin(θ – 350) --------(i)
Resolving the forces along the plane,
∑Fx= 0
Pcos(θ – 350) - F – 500sin35 = 0
Therefore, Pcos(θ – 350) - 122.87 + 0.3Psin(θ – 350) -286.79 = 0
P
FBD
500 N
F
N
500sin35
500cos35
350
350
motion
350
500
+X
-X
+Y
-Y
(θ – 350)

## Slide 40
P[cos(θ – 350) + 0.3sin(θ – 350)] = 409.66
P = 409.66/[cos(θ – 350) + 0.3sin(θ – 350)] ----(A)
For P to be minimum, cos(θ – 350) + 0.3sin(θ – 350)
Should be maximum i.e
d/dθ [cos(θ – 350) + 0.3sin(θ – 350)] = 0
Therefore -sin(θ – 350) + 0.3cos(θ – 350) = 0
sin(θ – 350)/cos(θ – 350) = 0.3
tan(θ – 350) = 0.3
θ = 51.70
P
FBD
500 N
F
N
500sin35
500cos35
350
350
motion
350
500
(θ – 350)

## Slide 41
From (A)
Pmin = 409.66/[cos(16.70) + 0.3sin(16.70)] = 392.38 N
Pmin = 392.38 N
P
FBD
500 N
F
N
500sin35
500cos35
350
350
motion
350
500
(θ – 350)

## Slide 42
Case (ii) to keep it from moving down
Since the block tends to move down the plane, the frictional force will be acting up the plane. i.e µS = 0.3
P
FBD
500 N
FA
N
500sin35
500cos35
350
350
motion
350
500
+X
-X
+Y
-Y
(θ – 350)

## Slide 43
From case(i) F = 122.87 – 0.3Psin(θ – 350)
Resolving the forces along the plane,
Pcos(θ – 350) + F – 500sin35 = 0
Pcos(θ – 350) + 122.87 - 0.3Psin(θ – 350) -286.79 = 0
Pcos(θ – 350) – 0.3Psin(θ – 350) = 163.92
P[cos(θ – 350) – 0.3sin(θ – 350)] = 163.92-----(B)
For P to be minimum,
d/dθ [cos(θ – 350) – 0.3sin(θ – 350)] = 0
i.e -sin(θ – 350) - 0.3cos(θ – 350) = 0
tan(θ – 350) = - 0.3
θ = 18.30
FBD
500sin35
500cos35
350
500
P
500 N
FA
N
350
motion
350
(θ – 350)

## Slide 44
From (B)
Pmin = 163.92/[cos(-16.7) – 0.3sin(-16.7)] = 157.0 N
Pmin = 157.0 N
FBD
500sin35
500cos35
350
500
P
500 N
FA
N
350
motion
350
(θ – 350)

## Slide 45
Problem 5.0
A body resting on a rough horizontal plane, required a pull of 180 N inclined at 30° to the plane just removed it. It was found that a push of 220 N inclined at 30° to the plane just removed the body. Determine the weight of the body and the coefficient of friction.

## Slide 46
Solution: Let ‘W’ be the weight of body in N. When a pull of 180 N is applied, its FBD is as shown.
∑Fx= 0
180cos300 – F = 0
F = 155.88 N
∑Fy= 0
N + 180sin300 – W = 0
N = W – 90
But F = µN
155.88 = µ(W – 90) -----(i)
180 N
FBD
W
F
N
300

## Slide 47
When a push of 220 N is applied
∑Fx= 0
F - 220cos300 = 0, F = 190.52 N
∑Fy= 0
N - 220sin300 – W = 0
N = W +110 But F = µN
190.52 = µ(W + 110) -----(ii)
Dividing (i) by (ii)
(155.88 / 190.52) = µ(W – 90) / µ(W + 110)
0.818W + 90 = W – 90
0.181W = 180 or W = 989 N
Now from (ii) µ = 0.173
220 N
FBD
W
F
N
300

## Slide 48
Problem 6.0
Find the maximum tension in the cord shown in figure, if the bodies have developed full friction.

## Slide 49
Solution: for the tension to occur in the cord, 100 N block should move up the plane and 400 N block should move down the plane.
Considering the equilibrium of the block resting on 300 incline plane its FBD is as shown.
FBD
400 N
+X
-X
+Y
-Y
F1
N1
300
400sin30
400cos30
300
400 N
300
motion
T

## Slide 50
Resolving all the forces perpendicular to the plane
N1 – 400cos30 = 0
i.e N1 = 346.41 N
Resolving all the forces along the plane
400sin30 – F1 – T = 0
T = 165.36 N
FBD
400 N
F1
N1
300
300
motion
T

## Slide 51
Now considering equilibrium of 100 N block, the tension in the cord Tl and frictional forces are shown in the figure.
T
FBD
100 N
F2
N2
100sin45
100cos45
450
450
motion
450
100 N
T1

## Slide 52
Resolving all the forces perpendicular to the plane
N2 – 100cos45 = 0
i.e N2 = 70.70 N
Resolving all the forces along the plane
T – Tl – F2 – 100sin45 = 0
But F2 = µN2 = 14.14 N
T1 = 80.52 N
T
FBD
100 N
F2
N2
450
motion
450
T1

## Slide 53
Problem 7.0
Two blocks A and B weighing 1500 N & 1000 N, and connected by a string passing over a smooth pulley, rest on a 60° inclined plane and a horizontal plane, the block B being subjected to an external force P as shown in figure. If the coefficient of friction be 0.25 under the blocks, find the least value of P to drag the block A up the plane.

## Slide 54
Solution: Consider the equilibrium of block A. since it has tendency to move up the plane, frictional force acts down the plane. Let TA be the tension in the string.
TA
FBD of block A
1500 N
FA
NA
1500sin60
1500cos60
600
600
motion
600
1500
+X
-X
+Y
-Y

## Slide 55
Consider equilibrium of block A
Resolving the forces perpendicular to the plane
∑Fy= 0
NA – 1500cos60 = 0
NA = 1500cos60 = 750 N
WKT FA = µANA = 0.25 * 750
FA = 187.5 N
Resolving the forces parallel to the plane
∑Fx= 0
TA - FA – 1500sin60 = 0
TA = 187.5 + 1500sin60
FBD of block A
1500 N
FA
NA
1500sin60
1500cos60
600
600
motion
600
1500 N
+X
-X
+Y
-Y
TA

## Slide 56
TA = 187.5 + 1299
TA= 1486.5 N
FBD of block A
WA
FA
NA
WAsin60
WAcos60
600
600
motion
600
WA
+X
-X
+Y
-Y
TA

## Slide 57
Psinθ
Pcosθ
TA
1000 N
FB
NB
motion
θ
P
θ
P
FBD of block B

## Slide 58
Consider equilibrium of block B
Resolving the forces parallel to the plane
∑Fx= 0
-TA - FB + Pcosθ = 0
WKT FB = µBNB
-1486.5 – 0.25NB + Pcosθ = 0 -----(i)
Resolving the forces perpendicular to the plane
∑Fy= 0
NB – 1000 + Psinθ = 0
NB = 1000 –Psinθ -----(ii)
Psinθ
Pcosθ
TA
1000 N
FB
NB
motion
θ
P
θ
P
FBD of block B

## Slide 59
Substituting (ii) in (i)
-1486.5 – 0.25(1000 – Psinθ) + Pcosθ= 0
Pcosθ+0.25Psinθ = 1736.54
Therefore P = 1736.5/(cosθ + 0.25sinθ)
For P to be minimum , (cosθ + 0.25sinθ) should be maximum
i.e, d/dθ (cosθ + 0.25sinθ) = 0
i.e – sinθ + 0.25cosθ = 0
Or sinθ = 0.25cosθ
Psinθ
Pcosθ
TB
1000 N
FB
NB
motion
θ
P
θ
P
FBD of block B

## Slide 60
Or tanθ = 0.25
θ = 14.030
Pmin = 1736.5/(cosθ + 0.25sinθ)
Pmin = 1684.65 N

## Slide 61
Problem 8.0
Two blocks A & B, connected by a horizontal rod by frictionless hinges, are supported on two rough planes as shown in figure. The coefficients of friction are 0.3 between block A and the horizontal surface & 0.4 between block B and the inclined surface. Block B weighs 1000 N. What is the smallest weight of block A that will hold the system in equilibrium ?

## Slide 62
Solution: Since the block B has a tendency to move down the plane, frictional force acts up the plane. There will be reaction from block A through the rod. FBD of block B is as shown
RA
1000 N
F
NB
600
FBD of block B

## Slide 63
Resolving all the forces perpendicular to the plane
NB – 1000cos60 – RAsin60 = 0
i.e NB = 500 + 0.866RA
But F = µNB = 0.4(500 + 0.866RA)
F = 200 + 0.3464RA-----(i)
Resolving all the forces along the plane
F – 1000sin60 + RAcos60 = 0
From (i) putting the value of F
200 + 0.3464RA- 866 + 0.5RA = 0
RA = 786.86 N
RA
1000 N
F
NB
600
FBD of block B

## Slide 64
Considering equilibrium of block A its FBD is as shown in figure.
Let W be the weight of block A
Resolving all the forces perpendicular to the plane
∑Fy= 0
NA = W
Resolving all the forces along the plane
∑Fx= 0
F = 786.86 N
But F = µNA
786.86 = 0.3W
W = 2622.87 N
786.86 N
W
F
NA
motion
FBD of block A

## Slide 65
Problem 9.0
The coefficients of friction is 0.30 between all the surfaces of contact. Block C & D weigh 1000 N & 1500 N respectively. Determine the smallest force required to start block D moving if (i) Block C is restrained by cable AB as shown in figure.(ii) cable AB is removed.
P
B
A
C
D

## Slide 66
Solution: Case(i) Consider the equilibrium of block C. when block D moves to the right, because of the cable AB. Block C moves to the left.
Hence the friction force acts to the right. If T is the tension
In AB, its FBD is as shown .
Applying ∑Fy= 0, ND = 1000 N.
∑Fx= 0, FD = T
µND = T
0.3 * 1000 = T
T = 300 N.
T
1000 N
FD
ND
motion
FBD of block C

## Slide 67
Consider the equilibrium of block D.
Applying ∑Fy = 0, NG = 2500 N.
But FG = µNG = 0.3 * 2500 = 750 N
∑Fx= 0, P – 300 – FG = 0
P = 300 + 750 = 1050 N
P
ND+1500 N
FG
NG
motion
FBD of block D
300 N

## Slide 68
Case(ii) when cable AB is absent
Applying ∑Fy= 0, NG = 2500 N.
But FG = µNG = 0.3 * 2500 = 750 N
∑Fx= 0,
P - FG = 0
P = 750 N
P
2500 N
FG
NG
motion
FBD of block D

## Slide 69
Application to ladder problems.
A ladder resting on ground and leaning against wall is a typical case of friction problem in non concurrent coplanar system. Here three equations of equilibrium are available,
∑Fx = 0; ∑Fy = 0; ∑M = 0.
From law of static friction we have µ = F/N
Thus using these three equations, problems on ladder is solved.

## Slide 70
Problem 10
A ladder of length 4.0 m and weighing 200N is placed against a vertical wall as shown in figure. The coefficient of friction between the wall and the ladder is 0.2 and that between the floor and the ladder is 0.3. the ladder in addition to its own weight has to support a man weighing 600 N at a distance of 3.0 m from A. calculate the minimum horizontal force to be applied at A to prevent slipping.
600 N
B
A
4 m
3 m
200 N
2 m
600

## Slide 71
FBD of ladder is as shown in figure. Let P be the force to be applied at A.
∑MA= 0,
200 * 2cos60 + 600 * 3cos60 – NB * 4sin60 – FB * 4cos60 = 0
But FB = µNB = 0.2 NB
Therefore 200 + 900 – 3.464NB - 0.4NB = 0
3.864NB = 1100 or NB = 284.68 N
FB = 0.2 * 284.68 = 56.93 N
∑Fy= 0, NA + FB – 200 – 600 = 0
NA = 743.07 N
600 N
B
A
FB
200 N
NB
FA
P
NA
FBD
600 N
B
A
4 m
3 m
200 N
2 m
600

## Slide 72
∑Fx= 0, P + FA - NB –= 0
P = 284.68 – 0.3* 743.07 = 61.76 N
P = 61.76 N
600 N
B
A
FB
200 N
NB
FA
P
NA
FBD

## Slide 73
Problem 11
A uniform ladder AB of length 3.0 m and weight 200 N rests with the end B against rough vertical wall and the end A on the level ground. If the wall and the ground are equally rough and the coefficient of friction is 0.5, find the limiting position of equilibrium.
B
A
3 m
200 N
1.5 m
θ

## Slide 74
Let the ladder makes an angle θ with horizontal in limiting equilibrium condition.
FBD of the ladder is as shown
Applying ∑Fx = 0, FA – NB = 0 or FA = NB
But FA = µNA
therefore µNA = NB
NA = NB / 0.5 = 2NB -----(i)
∑Fy = 0,
NA – 200 + FB = 0 or 2NB + 0.5NB = 200
NB = 80 N
B
A
FB
200 N
NB
FA
NA
FBD
B
A
3 m
200 N
1.5 m
θ

## Slide 75
Applying ∑MA= 0,
200 * 1.5cosθ – NB * 3sinθ – 0.5NB * 3cosθ = 0
300cosθ – 240sinθ – 120cosθ = 0
180cosθ = 240sinθ
tanθ = 180/240 = 0.75
Therefore θ = 36.860
The ladder will be in limiting equilibrium when it makes 36.860
with horizontal.
B
A
FB
200 N
NB
FA
NA
FBD
B
A
3 m
200 N
1.5 m
θ

## Slide 76
Problem
A ladder of length 4.0 m and weighing 200N is placed against a vertical wall as shown in figure. The coefficient of friction between the wall and the ladder is 0.2 and that between the floor and the ladder is 0.3. the ladder in addition to its own weight has to support a man weighing 600 N at a distance of 3.0 m from A. calculate the distance x measured along the ladder from A at which horizontal force P = 80 N to be applied at A to prevent slipping.
600 N
B
A
4 m
3 m
200 N
2 m
600
P = 80 N
x

## Slide 77
∑Fx= 0, 80 + FA – NB = 0
FA – NB = - 80
0.3 NA - NB = - 80 ------(i)
∑Fy= 0, NA + FB – 200 – 600 = 0
NA + FB = 800
NA + 0.2 NB= 800 ------(ii)
Solving (i) & (ii) we get
NA = 739.62 N & NB = 301.88 N
600 N
B
A
FB
200 N
NB
FA
80 N
NA
FBD

## Slide 78
FA = 0.3 * 739.62 = 221.88 N
FB = 0.2 * 301.88 = 60.37 N
∑MA= 0,
200 * 2cos60 + 600 * 3cos60 – NB * 4sin60 – FB * 4cos60
+ 80 * xsin60= 0
Therefore 200 + 900 – 1045.74- 120.74 + x80sin60 = 0
x = 66.48/(80sin60)
x = 0.96 m
600 N
B
A
FB
200 N
NB
FA
80 N
NA
FBD
600 N
B
4 m
3 m
200 N
2 m
600
P = 80 N
x

## Slide 79
Applications to wedge problems
Wedges are small piece of hard materials with two of their opposite surfaces are not parallel to each other. They are used to slightly lift heavy blocks, machinery, precast beams etc. for making final alignment or to make place for inserting lifting devices.
Here weight of the wedge is small compared to the weight lifted. Hence in all the problems weight of the wedge is neglected, unless it is specified.
In the analysis instead of considering normal reaction & frictional force independently, it is advantageous to take the resultant of these two forces.

## Slide 80
If ‘F’ is the limiting friction, ‘N’ be
the normal reaction, then ‘R’ will
be the resultant making limiting
Angle of friction with the normal.
F1
W
R1
θ
N1
N2
R2
F2
θ
F3
R3
θ
N3
P
R2
Block
Wedge

## Slide 81
Problem 12
A block weighing 1500 N is to be raised by means of a 10° wedge. Assuming the coefficient of friction between all the contacting surfaces to be 0.30, determine what minimum horizontal force P should be applied to raise the block?

## Slide 82
Solution: Coefficient of friction µ = 0.3
At limiting equilibrium tanθ = µ
tanθ = 0.3
θ = 16.690
Consider the equilibrium of block when the wedge
is pushed inside, the block slides upwards & towards right also
FBD of block is as shown.
R1 makes an angle θ with horizontal & R2 makes an angle (θ + 10) = 26.690
with vertical.
Since the three forces are concurrent we can apply Lami’s theorem to get R1 & R2
F1
1500 N
R1
θ
N1
N2
R2
F2
θ
FBD
R2
26.690
R1
16.690
1500 N

## Slide 83
R1/sin(180-26.69) = R2/sin(90-16.69) = 1500/sin(90+26.69+16.69)
R1/sin(153.31) = 1500/sin(133.38)
R1 = 926.98 N
R2/sin(73.39) = 1500/sin(133.38)
R2 = 1976.97 N
F1
1500 N
R1
θ
N1
N2
R2
F2
θ
FBD
R2
26.690
R1
16.690
1500 N

## Slide 84
Now consider the equilibrium of wedge
R2/sin(90+16.69) = R3/sin(90+26.69) = P/sin(180-26.69-16.69)
1976.97/sin(106.69) = P/sin(136.62)
P = 1417.56 N
F3
R3
θ
N3
P
R2
26.690
FBD
R2
26.690
R3
16.690
P

## Slide 85
Problem 13
One end of a beam B, of uniform cross section weighing 1200 N is hinged & the other end is lifted by a 15 wedge. The lower face of the wedge A is horizontal on a horizontal support. The coefficient of friction is 0.36 at the upper surface of the wedge & is 0.25 at the lower surface. Find the horizontal force required to push the wedge under the beam.

## Slide 86
Solution: On the upper surface of the wedge, µ1 = 0.36 = tanϕ1
ϕ1 = 19.790
On lower surface of the wedge, µ2 = 0.25 = tanϕ2
ϕ2 = 14.030
Consider the equilibrium of beam. The reaction of wedge R1 on the beam makes an angle of 19.790+ 150 = 34.790 with vertical as shown in FBD.
∑Mc= 0, 1200 * (l/2) - R1cos34.790 * l = 0
R1 =600/cos34.790 = 730.30 N
ϕ1
1200 N
Rcx
150
N1
R1
F1
C
FBD
Rcy
l

## Slide 87
Now Consider the equilibrium of wedge. FBD is as shown,
Applying Lamis’s theorem
R2/sin(90+34.79) = 730.6/sin(90+14.03) = P/sin(180-34.79-14.03)
R2/sin(90+34.79) = 730.6/sin(90+14.03)
R2 = 618.44 N
730.6/sin(90+14.03) = P/sin(180-34.79-14.03)
P = 566.78 N
14.030
P
FBD
34.790
R2
730.6 N
150
730.6
34.790
R2
14.030
P

## Slide 88
Problem
Determine the horizontal force P to start 4000 N wedge, to the right. The angle of friction is 200 at all the contact surfaces. Refer fig. also find the reaction from inclined surface.

## Slide 89
Problem 2.0
A force P = 350 N acts as shown on the block of weight W = 500 N which is resting on an inclined plane. The coefficients of friction between block and inclined plane are µs= 0.4 & µk= 0.3 Determine whether the block is in equilibrium and find the value of the frictional force. Take θ = 300
P
θ

## Slide 90
Solution:
Let us first draw the Free body diagram (FBD) and understand different forces and reactions acting on the block.
P = 350 N
θ
FBD
W = 500 N
+X
-X
+Y
-Y
N
W = 500 N
500cosθ
500sinθ
θ

## Slide 91
Net force acting along the plane,
350 – 500sinθ
= 100 N (acting up the plane)
Hence the body is having tendency to move up the plane.
For equilibrium frictional force required is Freq = 100 N acting
Down the plane.
Net force acting perpendicular to the plane,
-500cos30 + N = 0
N = 433.01 N
Frictional force at limiting equilibrium condition is
Fm= µsN
Fm= 0.4*433.01
= 173.20 N
Since Fm> Freq the block will be in equilibrium.
value of the frictional force; Fs = 173.20 N and it acts in the downward direction.
P = 350 N
θ
W = 500 N
N

## Slide 92
Thank You